Lining a Women's Lacrosse Field

Important notes to read first:

- Girl’s Lacrosse Fields are lined incorrectly too often. Everything is in the rule book, but it can still be confusing. These instructions offer a step-by-step method for lining quickly and accurately.

- Familiarize yourself with the diagrams before you begin. Follow the written STEPS (pg 2) in sequence, rather than work only from the diagram. Read all notes and directions first before beginning.

- The lines are part of the "area". The Goal Circle (GC) paint is "in" the GC; the 12m fan paint is "in" the fan; the 8m paint is "in" the arc.

- Often it is helpful to mark the field down correctly yourself, even if lightly - and then let your grounds crew darken it with a machine and maintain it.  Someone should plan on re-painting the lines at least every 2 weeks, before they disappear; it is much easier to maintain the markings than re-measure.

- Color. If different sports are using the field, blue, red, black and orange are easiest to see.  White is acceptable but becomes more difficult to see in areas of sparse grass. Stay away from yellow – it is very difficult to see under night lights and when the sun is low in the sky (mornings and late afternoons).

- Technique: One person: lightly mark dashed lines, then go over with paint striper. Two people: The person measuring should precede the person painting. The measurer should always be moving first and the painter follow. Just show where the mark is and keep moving, 1-2 feet ahead of the painter (dashed lines or dots).

- Points (A,B,C,D,E,G) on the diagrams are actually "points", not lines. Example: "D" is at the middle, front side the goal line. "A" is the middle, back side of the GC. "G" is of middle of the 8m Arc. "B" is the outside edge of the GC paint on the backside of the GLE.

- The dashed lines are for illustration only and are not painted.

- VERY handy, but not necessary: If your measuring tape has a blank side, mark and label it in 7 places (or measure and mark a plastic-coated dog run steel cable):

8' 6” - Goal Circle	 10’ - Center Line 13'2"	13’2” – 4 m		 30’ - Center Circle

34’10” - 8m Arc 	40’ 3” - A to C (diag) 		47’9” - 12m Fan

- In the following: “mark” means put some kind of semi-permanent paint down that is the width of the final line. A “small mark" is something only big enough to be visible – an inch or two. Scuff out later.

- When using spray paint, mark the spot, then lift the tape measure away before you spray - otherwise you paint your tape measure.

- For the following instructions, the “front” side of anything means closer to the middle of the field, the “back” side means farther away from the middle, “inside” means closer to the "Main Axis" of the field.

- The instructions assume you are working on plain grass with no other markings (eg. a football field) to guide you. If you already have some markings, eg. football field, they can help you keep things straight, but you should still follow the instructions, step by step.

Equipment.

- 3 easily visible “stakes”. These can be anything that will stand out and stick up from the surface so they can be seen and lined up as far as 100 yards apart: orange tent stakes, orange cans of paint, 1” wooden dowels or stakes, brightly painted.

- Corkscrew dog anchor for point D and center of center circle.

- Measuring tape of at least 100 ft. If you have 250-300, that is great.

- Paint. 12 cans for a regulation field.  Final markings should be 2” – 4” wide.

- Paint Striper

- Paint wand and "striping" paint can be used for circles, arcs and fans.  Wrap the tape measure around the bottom of the wand and walk fast while spraying and keeping the measuring tape tight.

- Assistance. You can line a field by yourself, but you will greatly reduce your time if you have a helper or two.

STEPS in lining a women’s lacrosse field

Follow in sequence. Instructions are BOLD. Everything else is just an explanation. Once you get the hang of it, you need only the bold steps.

1.  Mark main axis of field

Place 3 "stakes" in a straight line: 2 at center of each goal line and 1 at center of field. Goal Stakes are 90 yds apart, with 10 yds from goal line to endline. The line formed by these 3 stakes is the "Main Axis". (Hint: you can step the distances off. Pace off 50 yards on a football field to find your pace count.)

2. Goal Circle (GC)

Use corkscrew dog anchor and screw into ground at point D. Mark a circle of radius 8’ 6” (outside edge of the paint is 8’6” from point D). For convenience, put a small mark at the center back of the GC (or stick a stake in the ground - this is point A). Put a small “T” right behind D in case it moves while working. It will get painted over.

3. Goal Line Extended (GLE) and 12m fan

a. KEEP TAPE AT D. Measure 47’ 9” to either E. Paint the GLE from B to E. (paint on front side of the tape). Make a 1 foot mark, perpendicular to and on the front side of the GLE, at 34’ 10”.

b. KEEP TAPE AT D. Make the 12m Fan from E to E at 47’ 9”. (outside edge of paint at 47’ 9”). After you get to other E, paint that GLE back to B and a 1’ hash mark at 34’ 10”.

4. 8m ARC

a. MOVE THE END OF THE TAPE FROM POINT D TO POINT A; measure 40’ 3” to C. Tape should intersect the GC at the GLE. It should read exactly 12 feet where it crosses at B - using outside edge of GC at A and B.

b. Paint from B to C; along the inside edge of the tape.

c. Repeat 3a. and 3b. to form the other side of the 8m Arc.

d. MOVE THE END OF THE TAPE BACK TO POINT D; the front edge of the goal line, centered.

e. Measure 34’10” to C. Paint the 8m Arc from C to the other 8m Side. (outside edge of paint should be at 34' 10")

5. Goal Line

KEEP TAPE AT D. Paint a 6’ goal line immediately behind D (3' to either side).

6. Hash Marks

a. Look down Main Axis and find MIDDLE of 8m Arc. Place 1’ CENTER Hash Mark at G.

b. Measure 13’ 2” (4m) from G, in both directions, and place 2nd Hash Marks on the 8m Arc. MOVE THE TAPE to either 2nd mark and place 3rd Hash Mark 13’ 2” from the 2nd Hash Mark. MOVE THE TAPE to the 3rd Mark and place a 4th Mark 13’ 2” from the 3rd Hash Mark where the 8m Arc would have extended. Do this on both sides of the 8m Arc (floating hash marks).

7. Restraining Line (RL)

Make a small mark 90’ from D on Main Axis. Make another small mark 90’ from either E measuring parallel to Main Axis. These two marks should be exactly 47’ 9” apart - correct the second mark as necessary. Paint RL the width of the field, intersecting these two marks.

8. Center Circle  Paint a circle 30’ in radius. Also, paint the centerline, approx 10’ wide.

9. Sidelines and Endlines. Make solid lines to indicate playing boundaries around the sides and ends of the field. They must be 4m from any change of surface, fence, obstacle, or the end of defined playing space.